Military Potentiometers Index (Ctrl+ click to follow links)

RV4 – 2W, ¼’’ Shaft

2RV7 – 2W, ¼’’ Shaft, Multiple element

RV2 – 1W, ¼’’ Shaft

RV6 – 0.5W, 1/8’’ Shaft, Solder Wire

RV8 – 0.5W, 1/8’’ Shaft, PCB Terminals

RV5 – 0.5W, 1/8’’ Shaft, 19mm Diam., Radial Terminals

RV4

|  | MIL Style RV4 Specs Precision Series K - 2 Watt 1/4" shaft diameter |
| --- | --- |

| Precision series K/RV4 potentiometers are suitable for both military and commercial applications. They can easily be customized to meet special requirements. |
| --- |
| Features hot molded carbon element gold-plated terminals stainless-steel shaft and housing quality meeting or exceeding MIL-R-94 - QPL listed | Options custom shafts and bushings special tapers fourth (center) terminal high life attached switch |
| Electrical Specifications Resistance range, linear taper: 50 to 5 Meg Resistance range, logarithmic taper: 150 to 1 Meg Resistance tolerance: ±10% or ±20% Resistance taper: linear, logarithmic, reverse logarithmic; other tapers by special order Power rating: 2 watts at 70°C derated to 0 watts at 120°C Insulation resistance: dry: 10K Meg wet: 100K Meg Dielectric strength: 900 V RMS at sea level Operating voltage: 500 V, subject to power rating | Mechanical Specifications Mechanical rotation: 314° Operating torque: 1 oz/in to 6 oz/in Rotational life: 25,000 cycles Environmental Specifications Operating temperature: -65°C to +125°C Resistance to soldering heat: 350°C for 5 seconds Humidity range: per MIL-R-94 Vibration range: per MIL-R-94 Shock resistance: per MIL-R-94 Load life: 1000 hours at 70°C |

| Ordering Information - Military Part numbers |
| --- |
| style: | bushing: | switch: | temperature and moisture characteristics: | shaft style: | shaft length: | resistance value: | taper and tolerance: |
| RV4 = MIL style RV4 | N = standard L = locking S = panel & shaft seal | A = without switch B = SPST switch | Y = as per MIL-R-94 | S = slotted F = flatted | B = 1/2" A = 5/8" D = 7/8" G = 1 1/4" J = 2" K = 2 1/2" | total resistance value in : first two digits significant, third digit = number of zeroes | A = linear 10% B = linear 20% C = logarithmic 10% D = logarithmic 20% E = reverse logarithmic 10% F = reverse logarithmic 20% |
| Example: RV4NAYSB000A note: not all part number combinations are valid |

2RV7

|  | MIL Style 2RV7 Specs Precision Series KK - 2 Watt multiple element 1/4" shaft diameter |
| --- | --- |

| Precision series KK/2RV7 potentiometers are suitable for both military and commercial applications requiring multiple elements. They can easily be customized to meet special requirements. |
| --- |
| Features hot molded carbon element gold-plated terminals stainless-steel shaft and housing quality meeting or exceeding MIL-R-94 - QPL listed | Options custom shafts and bushings special tapers fourth (center) terminal concentric shafts attached switches |
| Electrical Specifications Resistance range, linear taper: 50 to 5 Meg Resistance range, logarithmic taper: 150 to 1 Meg Resistance tolerance: ±10% or ±20% Resistance taper: linear, logarithmic, reverse logarithmic; other tapers by special order Power rating: 2 watts at 70°C derated to 0 watts at 120°C Insulation resistance: dry: 10K Meg wet: 100K Meg Dielectric strength: 900 V RMS at sea level Operating voltage: 500 V, subject to power rating | Mechanical Specifications Mechanical rotation: 314° Operating torque: 1 oz/in to 12 oz/in Rotational life: 25,000 cycles Environmental Specifications Operating temperature: -65°C to +125°C Resistance to soldering heat: 350°C for 5 seconds Humidity range: per MIL-R-94 Vibration range: per MIL-R-94 Shock resistance: per MIL-R-94 Load life: 1000 hours at 70°C |

| Ordering Information - Military Part numbers |
| --- |
| style: | bushing: | temperature and moisture characteristics: | shaft style: | shaft length: | resistance value: | taper and tolerance: |
| 2RV7 = MIL style 2RV7 | N = standard L = locking S = panel & shaft seal | Y = as per MIL-R-94 | S = slotted F = flatted | B = 1/2" A = 5/8" D = 7/8" G = 1 1/4" J = 2" K = 2 1/2" | total resistance value in : first two digits significant, third digit = number of zeroes | A = linear 10% B = linear 20% C = logarithmic 10% D = logarithmic 20% E = reverse logarithmic 10% F = reverse logarithmic 20% |
| Example: 2RV7NYSD103103A note: not all part number combinations are valid |

RV2

|  | MIL Style RV2 Specs Precision Series N - 1 Watt 1/4" shaft diameter |
| --- | --- |

| Precision series N/RV2 potentiometers are suitable for both military and commercial applications. They can easily be customized to meet special requirements. |
| --- |
| Features hot molded carbon element gold-plated terminals stainless-steel shaft one piece brass housing quality meeting or exceeding MIL-R-94 - QPL listed | Options custom shafts and bushings special tapers fourth (center) terminal attached switches |
| Electrical Specifications Resistance range, linear taper: 100 to 5 Meg Resistance range, logarithmic taper: 150 to 1 Meg Resistance tolerance: ±10% or ±20% Resistance taper: linear, logarithmic, reverse logarithmic; other tapers by special order Power rating: 1 watt at 70°C derated to 0 watts at 120°C Insulation resistance: dry: 10K Meg wet: 100K Meg Dielectric strength: 900 V RMS at sea level Operating voltage: 500 V, subject to power rating | Mechanical Specifications Mechanical rotation: 300° Operating torque: 1 oz/in to 6 oz/in Rotational life: 25,000 cycles Environmental Specifications Operating temperature: -65°C to +125°C Resistance to soldering heat: 350°C for 5 seconds Humidity range: per MIL-R-94 Vibration range: per MIL-R-94 Shock resistance: per MIL-R-94 Load life: 1000 hours at 70°C |

| Ordering Information - Military Part numbers |
| --- |
| style: | bushing: | switch: | temperature and moisture characteristics: | shaft style: | shaft length: | resistance value: | taper and tolerance: |
| RV2 = MIL style RV2 | N = standard L = locking S = panel & shaft seal | A = without switch B = SPST switch | Y = as per MIL-R-94 | S = slotted F = flatted | B = 1/2" A = 5/8" D = 7/8" G = 1 1/4" J = 2" K = 2 1/2" | total resistance value in : first two digits significant, third digit = number of zeroes | A = linear 10% B = linear 20% C = logarithmic 10% D = logarithmic 20% E = reverse logarithmic 10% F = reverse logarithmic 20% |
| Example: RV2NAYSD751C note: not all part number combinations are valid |

RV6

|  | MIL Style RV6 Specs Precision Series S - 1/2 Watt 1/8" shaft diameter |
| --- | --- |

| Series S/RV6 potentiometers are ideal for applications requiring high reliability and a compact size. |
| --- |
| Features hot molded carbon element one piece housing and bushing stainless-steel shaft compact size quality meeting or exceeding MIL-R-94 - QPL listed | Options special tapers custom shafts and bushings customer specified marking |
| Electrical Specifications Resistance range, linear taper: 100 to 5 Meg Resistance range, logarithmic taper: 150 to 1 Meg Resistance tolerance: ±10% or ±20% Resistance taper: linear, logarithmic, reverse logarithmic; other tapers by special order Power rating: 0.5 watts at 70°C derated to 0 watts at 120°C Insulation resistance: dry: 10K Meg wet: 100K Meg Dielectric strength: 750 V RMS at sea level Operating voltage: 350 V, subject to power rating | Mechanical Specifications Mechanical rotation: 295° Operating torque: 0.5 oz/in to 6 oz/in Rotational life: 25,000 cycles Environmental Specifications Operating temperature: -65°C to +125°C Resistance to soldering heat: 350°C for 5 seconds Humidity range: per MIL-R-94 Vibration range: per MIL-R-94 Shock resistance: per MIL-R-94 Load life: 1000 hours at 70°C |

| Ordering Information - Military Part numbers |
| --- |
| style: | bushing: | switch: | temperature and moisture characteristics: | shaft style: | shaft length: | resistance value: | taper and tolerance: |
| RV6 = MIL style RV6 | N = standard L = locking S = panel & shaft seal | A = without switch | Y = as per MIL-R-94 | S = slotted F = flatted | L = 3/8" B = 1/2" A = 5/8" D = 7/8" | total resistance value in : first two digits significant, third digit = number of zeroes | A = linear 10% B = linear 20% C = logarithmic 10% D = logarithmic 20% E = reverse logarithmic 10% F = reverse logarithmic 20% |
| Example: RV6LAYSA102C note: not all part number combinations are valid |

RV8

|  | MIL Style RV8 Specs Precision Series SPR - 1/2 Watt 1/8" shaft diameter |
| --- | --- |

| Series SPR/RV8 potentiometers are for PCB applications requiring a rugged potentiometer. |
| --- |
| Features hot molded carbon element board washable stainless steel shaft compact size quality meeting or exceeding MIL-R-94 - QPL listed | Options special tapers custom shafts and bushings location tab position customer specified marking |
| Electrical Specifications Resistance range, linear taper: 100 to 5 Meg Resistance range, logarithmic taper: 150 to 1 Meg Resistance tolerance: ±10% or ±20% Resistance taper: linear, logarithmic, reverse logarithmic; other tapers by special order Power rating: 0.5 watts at 70°C derated to 0 watts at 120°C Insulation resistance: dry: 10K Meg wet: 100K Meg Dielectric strength: 750 V RMS at sea level Operating voltage: 350 V, subject to power rating | Mechanical Specifications Mechanical rotation: 295° Operating torque: 0.5 oz/in to 6 oz/in Rotational life: 25,000 cycles Environmental Specifications Operating temperature: -65°C to +125°C Resistance to soldering heat: 350°C for 5 seconds Humidity range: per MIL-R-94 Vibration range: per MIL-R-94 Shock resistance: per MIL-R-94 Load life: 1000 hours at 70°C |

| Ordering Information - Military Part numbers |
| --- |
| style: | bushing: | switch: | temperature and moisture characteristics: | shaft style: | shaft length: | resistance value: | taper and tolerance: |
| RV8 = MIL style RV8 | N = standard L = locking S = panel & shaft seal | A = without switch | Y = as per MIL-R-94 | S = slotted F = flatted | L = 3/8" B = 1/2" A = 5/8" D = 7/8" | total resistance value in : first two digits significant, third digit = number of zeroes | A = linear 10% B = linear 20% C = logarithmic 10% D = logarithmic 20% E = reverse logarithmic 10% F = reverse logarithmic 20% |
| Example: RV8NAYSD252A note: not all part number combinations are valid |

RV5

|  | MIL Style RV5 Specs Precision Series T - 1/2 Watt 1/8" shaft diameter |
| --- | --- |

| Series T/RV5 potentiometers provide a low profile with lateral lug terminals. |
| --- |
| Features hot molded carbon element one piece housing and bushing stainless steel shaft quality meeting or exceeding MIL-R-94 - QPL listed | Options special tapers custom shafts customer specified marking |
| Electrical Specifications Resistance range, linear taper: 100 to 5 Meg Resistance range, logarithmic taper: 150 to 1 Meg Resistance tolerance: ±10% or ±20% Resistance taper: linear, logarithmic, reverse logarithmic; other tapers by special order Power rating: 0.5 watts at 70°C derated to 0 watts at 120°C Insulation resistance: dry: 10K Meg wet: 100K Meg Dielectric strength: 900 V RMS at sea level Operating voltage: 350 V, subject to power rating | Mechanical Specifications Mechanical rotation: 300° Operating torque: 1 oz/in to 6 oz/in Rotational life: 25,000 cycles Environmental Specifications Operating temperature: -65°C to +125°C Resistance to soldering heat: 350°C for 5 seconds Humidity range: per MIL-R-94 Vibration range: per MIL-R-94 Shock resistance: per MIL-R-94 Load life: 1000 hours at 70°C |

| Ordering Information - Military Part numbers |
| --- |
| style: | bushing: | switch: | temperature and moisture characteristics: | shaft style: | shaft length: | resistance value: | taper and tolerance: |
| RV5 = MIL style RV5 | N = standard L = locking | A = without switch | Y = as per MIL-R-94 | S = slotted | L = 3/8" B = 1/2" A = 5/8" D = 7/8" | total resistance value in : first two digits significant, third digit = number of zeroes | A = linear 10% B = linear 20% C = logarithmic 10% D = logarithmic 20% E = reverse logarithmic 10% F = reverse logarithmic 20% |
| Example: RV5NAYSD502A note: not all part number combinations are valid |